## Slide 1: Data Formats & Data Structures
Crossroads of Active Source and Broadband Structures
Justin Sweet
USArray Advanced Short Course, August 2017

## Slide 2: Variety of seismic deployments
Passive seismic – natural sources (earthquakes)
Tomography
  Regional and Global Scale
  Surface Wave
  Ambient Noise Tomography

## Slide 3: Variety of seismic deployments
Active seismic – artificial sources (explosives, hammer, etc.)
Figure from Karplus

## Slide 4: Variety of seismic data formats
Passive source
  SEED
  SAC
Active source
  SEG-Y, SEG-D, SEG-2
Both
  PH5

## Slide 5: SEED: Standard for the Exchange of Earthquake Data
International format, maintained by the FDSN
Includes both time series data and metadata stored separately
Comprehensive record of data recording process
200 page manual
  www.iris.edu/manuals/SEEDManual_V2.4.pdf
Convert SEED to other formats using rdseed
Three common variants:
SEED
Dataless
Mini-SEED

## Slide 6: SEED Structure
waveform data
raw data and embedded auxiliary information
Mini-SEED
binary (+ ASCII)
(full) SEED volume
control headers
dataless SEED
ASCII
SEED is constructed from defined structures called blockettes
SEED response information is specified as a cascade of
stages
Notes: Even though most SEED headers are in ASCII is is not readable, certainly not editable

## Slide 7: Comprehensive Metadata Representation
Notes: - The total system sensitivity is the product of all stage sensitivities and represents the scaling from ground units to digital samples in counts

## Slide 8: SAC: Seismic Analysis Code
Developed in 1980s by LLNL as a seismic data file format and processing package
Currently made available by IRIS DMC
Precision in timing and distance has improved beyond SAC single-precision capability
  For sample rates >0.01s and long record lengths, timing precision in SAC is inadequate
  Geographic values are marginally adequate (~1m precision)
Increasing SAC precision will change SAC header and has implications on existing programs
Addressing Precision Limitations in the Seismic Analysis Code (SAC) File Headers and Data Format from 2012 Eastern SSA presentation

## Slide 9: SAC: Seismic Analysis Code
Each SAC data file contains
  single data set – single data component recorded at a single station
  header record – describes the contents of the file
SAC binary format (most common)
Notes: Part of the motivation for developing ASDF stems from the fact that reading and writing SAC files for a large tomographic inversion practically brings a huge parallel file system to its knees due to the very large number of involved files.

## Slide 10: SEG-Y: Society of Exploration Geophysicists for storing data
Developed in 1970s for use by the active source community
Variety of flavors
  SEG-D, developed for field data
  SEG-P, developed for positional data
  SEG-Y, intended to be format for everybody
Recent release (rev 2.0, 2017)
  Higher capacity for trace data
  Microsecond time-stamp accuracy
  Higher-precision coordinates, depths, and elevation

## Slide 11: SEG-Y: Society of Exploration Geophysicists for storing data
What’s in a SEG-Y file?
  Text file header (green)
  Trace header (light blue)
  Actual data (purple)
Major limitation – Data & metadata stored together
  Cannot update metadata (headers) without re-archiving the entire dataset

## Slide 12: PH5: PASSCAL HDF5 format
Developed at PASSCAL beginning in early 2000s
Based on robust Hierarchical Data Format (HDF5) designed to store and organize large amounts of data
Stores data and metadata separately
  Frontload waveform data into DMC
  Efficient metadata updates
Allows access to parts of the data without needing to parse the entire file
Exposes active source data to DMC request tools

## Slide 13: PH5: PASSCAL HDF5 format
Why HDF5?
  20+ year history starting at NCSA
  Widely used & well supported
  Self-describing format
    Can create your own data organization
  Hierarchical
  Easy to edit
  Built-in compression
  Fast reading

## Slide 14: Format Usage: Field versus Archive
Different formats designed for different uses
  Eg. SEG-D (designed for field use) vs. SEG-Y (designed for archive and analysis)
Field priorities
  Easy to visualize
Archive priorities
  Highly-compressible
  Well-described

## Slide 15: PH5 & Kitchen Software Suite
Can we design a format the works well in both the field and in the archive?
PH5 – Format definition that describes the HDF5 file organization
Kitchen – Software suite that provides the tools to interface with PH5

## Slide 16: Field data  PH5  Archive
Data ingestion
  Waveform data ingested into PH5 using Kitchen suite tool (pforma)
  Metadata imported automatically for some raw data formats (e.g. SEG-D), or can be imported using Kitchen GUI tool (noven)
Data QC
  PH5Viewer – options to select gathers, time windows, reduction velocity, simple gain and plotting options
  Development of tool to confirm all data described by metadata and/or missing metadata

## Slide 17: Field data  PH5  Archive

## Slide 18: Field data  PH5  Archive

## Slide 19: Current DMC Interface

## Slide 20: PH5: PASSCAL HDF5 format

## Slide 21: User access to PH5 data at IRIS DMC
Current capability – Web page interface
  Allows for extraction of SEG-Y shot and receiver gathers, or SAC waveforms
  Once requests made, data available via ftp
Planned capability – webservices
  2 services: station and dataselect
    station – access to metadata identical to standard station webservice currently in use for SEED data
    dataselect – access to waveform data into mseed format
Once webservice is up and running, PH5 data will be accessible just like the rest of the DMC archive
  Exposed to DMC QC tools like MUSTANG
  Huge advance for active source data!

## Slide 22: PH5: Container for both active and passive data
Unlike earlier formats, PH5 is capable of holding active and passive data at the same time, as part of a single dataset.
Data extraction
  Active source can be output at SEG-Y
  Passive source can be output at mseed or SAC.

## Slide 23: Exercise: Let’s access the Wavefields dataset
DMC data access tools
  http://ds.iris.edu/ds/nodes/dmc/tools
List of experiments archived in PH5
  http://ds.iris.edu/pic-ph5/experiment_list.php
Presently, wavefields dataset is archived in miniseed
  Accessible via webservices
    Webservices info/syntax - http://service.iris.edu
    Local webservices access
      http://156.56.66.202:8080/fdsnws/dataselect/1

## Slide 24: Exercise: Let’s access the Wavefields dataset
Timeseries
  http://service.iris.edu/fdsnws/dataselect/1/
  Use the URL builder to plot data from
    Network: YW
    Station: 511
    Location: 01
    Channel: HHZ
    Starttime: 2016-07-13T00:00:00
    Endtime: 2016-07-13T12:00:00
  Add a bandpass filter from 2-10Hz
  Try modifying the URL to access the local copy of the data via webservice
    http://156.56.66.202:8080/fdsnws/dataselect/1