## Slide 1: Beam Forming Arrays
Charles A. Langston
Center for Earthquake Research and Information
University of Memphis

## Slide 4: Array Design Criteria
Station spacing
Array Diameter
Wave Correlation Distance
(as determined from regional arrays)
Notes: Array designs must sample the spatial wavefield a frequencies less than Nyquist frequency, which is related to average sensor spacing. The array Diameter must be greater than a wavelength of the wave under study. Results from regional arrays show that crustal and upper mantle phases generally decorrelate over a distance, a, which is roughly a single wavelength. Thus, regional array resolution is limited by this degradation in correlation distance since beam forming implicitly assumes that the underlying wave signal is identical over all array elements.

## Slide 5
Wave velocity v
i
Horizontal
Phase Velocity
Horizontal Slowness
0
D
Horizontal Wavelength

## Slide 6: Horizontal Wavenumber (Slowness) Spectra

## Slide 7
Notes: The ability to resolve two signals can be estimated using a 1D line array that is D long. The frequency-wavenumber power spectrum is a sinc function to the fourth power. If resolution is defined as separation at the half-width of the signal peak, then a minimum array diameter, D, can be estimated for a given difference in the target slowness. Here it is assumed that we want to separate two signals with a 10% slowness difference. The array diameter must be greater than 3 times the horizontal wavelength to do so. Thus, it is difficult for regional arrays to perform at this level since signal correlation degrades significantly over a single wavelength.

## Slide 8
Notes: This is a plot of of the needed array diameter to target wavelength ratio for different desired error thresholds. Smaller separations in slowness require greater array diameters.

## Slide 10: Array Slowness Response 0.3 to 1 Hz Bandpass Signal Power
Linear density scale
Logarithmic density scale (dB)

## Slide 11
Array Diameter > Wavelength

## Slide 12
Ideal
Actual
Is this possible?

## Slide 13
M4.2 Fairview, OK, Earthquake
Backazimuth = 262.5o
1 to 2 Hz
It actually works!
P waveforms
5 to 8 Hz