## Slide 1
Tucson SITS 2018 – Theo Laudat – 30/10/2018
Next generation products roadmap # B6
Notes: Thank you mister Chairman for this kind introduction (seulement si il y a une introduction ;-)
Aux states cela se fait beaucoup de se présenter au début
I am theo Laudat, thechnical manager of blueSeis product line from iXblue , And I am pleased to be there to let you know more about our brand new rotational seismometer called blueSeis-3A

## Slide 2
blueSeis-1C: Ultra-low-noise, 1component, sensor cold head
To be released, April 2019 @EGU Vienna
 | blueSeis-1C
Weight | 15kg
Height | 34mm
Diameter | 400mm
Price | TBD
Power consumption | 4W each 6W for 3
Self-noise | 5 nrad/s/√Hz
Very broadband | 0.001 Hz – 100 Hz
 | Sensor head | Electronic box
Power consumption | <1mW | 4W (1 sensor head) 6W (3 sensors head)
Time stamping | NA | Only disciplined serial data rate output
Data output | NA | Serial streaming
Data logging | NA | Outside (digitizer with serial input)
Signals
to measure
0.5 nrad/s sinus =>
200 nrad sinus @ 0.001Hz
nrad/s sinus =>
2 nrad sinus @ 10Hz
Applications
Seismology
Hydrology OBS seismometer denoising
Large instrument denoising
Planetology
Volcanology
… Any other ideas ?
Cabling
Battery
12V
240V
GNSS antenna
Laptop
Config°
Digitizer
12V
Serial
Power supply
Serial
1C
GNSS antenna
4W
<1mW
Battery
12V
240V
GNSS antenna
Laptop
Config°
Digitizer
12V
Serial
Power supply
Serial
3x1C
GNSS antenna
6W
<1mW
Characteristics

## Slide 3
blueSeis-3A Next Generation: smaller, lighter, and more versatile
To be released, April 2019 @EGU Vienna
 | blueSeis-3A | blueSeis-3A NG
Weight | 20kg | 18kg
Height | 350mm | 310mm
Diameter | 318 mm | 
Price | identical | 
Power consumption | 15W | ‘-e’ : 6W+4W ‘-s’ : 6W+2W
Selfnoise | 20 nrad/s/√Hz | 
Broadband | 0.01 Hz – 50Hz | 
Battery
12V
240V
GNSS antenna
Laptop
Config°
Data logger
12V
TCP/IP
Serial
Power supply
Data logging
3A-e
6W
4W
Battery
12V
240V
GNSS antenna
Laptop
Config°
Digitizer
12V
Serial
Power supply
Serial
3A-s
GNSS antenna
2W
6W
Cabling
Battery
12V
240V
GNSS antenna
Laptop
Config°
Data logger
12V
TCP/IP
Serial
Power supply
15W
3A
Characteristics
Versatil electronic box
 | 3A | 3A-e | 3A-s
Time stamping | Inside sensor | Inside box | Only disciplined serial data rate output
Data output | miniSEED streaming | SEEDlink server | Serial streaming
Data logging | Outside (datalogger) | Inside and outside | Outside (digitizer with serial input)
Should we ?
Have an omblic instead of connector out of the sensor ?
Have 3A-e and 3A-s options, maybe only one is enough ?
Have a smaller+cheaper+ligher sensor at 50nrad/s/√z ?