## Slide 1: Ultra low frequency Noise Properties from Analysis of Data from the Homestake 3D Broadband Array
Prof. Gary L. Pavlis
Ross Caton1
James Atterholt2
Department of Earth and Atmospheric Sciences
Indiana University
Frank Vernon, IGPP UCSD
David Thomson, Queens University
1Phd Student completing this year – great postdoc prospect
2Undergraduate – if he applies to your program you want him

## Slide 2: Acknowledgements
Collaborators for Homestake Experiment
  Vuk Mandic, Tanner Prestegard, Patrick Myers, University of Minnesota, Physics (Part of LIGO collaboration)
  Victor Tsai and Daniel Bowden, California Institute of Technology
Supported by National Science Foundation INSPIRE
Active source piggyback funded by NSF Geophysics
Sanford Underground Research Facility (SURF) at Homestake

## Slide 3: What does broadband mean?
The Road Less Traveled

## Slide 4: Key Point
The unexplored frontier: 30 minutes to 1 day period
  Very few instruments resolve ground noise in this band
  Arrays necessary to resolve ambiguity of marginal snr
  Homestake and PFO borehole data hint at scientific potential
The 1-10 Hz catastrophe
  USArray has shown 1 Hz P waves coherent over 1000+ km
  Since VELA we know 10 Hz signals are hard to stack over more than a wavelength
  For decades I blamed the weathered layer based on experience with JSP arrays
  Homestake active source experiments suggest problem may be more fundamental

## Slide 5: Homestake 3D Broadband Array
Mandic et al (2018) in press in SRL

## Slide 6: Underground Deployment
Hard rock mine
All in side rooms of various size
Utilized existing concrete from mine
Granite tiles attached to concrete with thinset
All STS-2 sensors
Standard PASSCAL Q330s

## Slide 7: LP band noise good, but not that special

## Slide 8: Below 100 s period are where these data are amazing
24 hours

## Slide 9: A Key Reason: Temperature stability
Surface
>50C range
Underground
< 1C range

## Slide 10: Underground example
10C
One year

## Slide 11: Low Frequency Spectrum Example
Earth tides
Lowest free oscillation
Earth “hum” modal lines
?

## Slide 12: Instrumentation Issues in this Band
Instrument response?
Mass recenters
How do we know we are measuring anything but electronic noise?
AR whitening filter
Transient filter
Array stack with jackknife error estimates to measure consistency
Issues
Our solution

## Slide 13: Instrument Response Correction?

## Slide 14: Prewhitening
Needed to test hypothesis of Thomson and Vernon that spectra in this band dominated by lines linked to solar modes
Assumption:
  lines are superimposed on a continuous background
  AR filter aims to remove background

## Slide 15: AR Prewhitening Operator
Sensor corner 110s =9090

## Slide 16: Transient Filter and Mass Recenters
Raw Data
Filtered
Note Scale Difference

## Slide 17: Importance of Transient Filter
Studying noise in this band requires a long time series
Frequency resolution scales with 1/length of time series
Try to find any broadband data without a mass recenter in 6 months or more of recording
The big earthquakes we love also will dominate any 1 year long spectrum – works for that too

## Slide 18: Importance of a BB array
Redundancy
  Do we see the same signal at all stations?
  Allows statistical error appraisal
Mass recenters don’t align and can be removed by robust stacking

## Slide 19: Simulation Validation: 3 lines in white noise
Signal-to-Noise ratio

## Slide 20: Data Example: Same time period
PFO
Homestake
300
400
Frequency (microHz)

## Slide 21: Final Approach: Hard core statistics
Idea:
  Spectra have a different texture than the they should be for white process
  Test using established statistical methods (our colleague David Thomson)
Methods
  Mixing parameter appraises fraction of data in lines
  D-statistic and Kolm0gorov-Smirnov test

## Slide 22: My God, It’s full of Lines!
3 s threshold

## Slide 23: 100-800 microHz -Summary
Coherent signals being recorded on underground sites at Homestake and to lesser extend PFO BB array
Spectra characterized by many overlapping pure harmonic lines
Correlates with increase in spectral amplitude trend below 800 microHz at Homestake (unclear if true elsewhere)
Working hypothesis we aim to test – G modes of the sun
  Modes modulate the solar wind
  Geomagnetic field couples to the ground or the seismometer OR
  Coherent signal on instruments created by direct magnetic coupling

## Slide 24: Super High Frequency Band (above about 100 Hz) Background
Oil and Gas exploration
  Predominantly 10-100 Hz
  Land versus marine data
  Universally known issue of weathered layer
  Land use of areal arrays for smoothing wavefield
Nuclear monitoring
  0.5-20 Hz band
  Arrays coherent only ~1 or 2 wavelengths
Contrast: short period P waves (1 Hz) are coherent over hundreds of wavelengths

## Slide 25: Hypotheses going into this experiment
Proven mostly true
Simple linear moveout
Anisotropic media
Wrong
Limited scattering – simple clean P and S pulses
Neglect the influence of the mine works
Could use plaster and sandbags to anchor sensors to rock

## Slide 26: 4850 experimental geometry

## Slide 27: Typical Shot Gather
P
S

## Slide 28: Signal and Noise Spectra
Power
Median noise

## Slide 29: Common Receiver Gathers from Walkaway (1 m shot spacing)

## Slide 30: Summary Points: super high frequency
Instrumentation
Anchoring a huge issue
4.5 Hz triaxial phones with spikes problematic
Cables we had available were a nightmare
Followup experiment would ideally use MEMS sensors with much higher spatial density
Anchor sensors with rock bolts
Science
Data
  Wild variations smaller than a wavelength
  Source and receiver side variation
Scattering
  May be higher than expected OR
  May be only seeing local site effects from drift damage zone
  May be fracture related
Fundamental question of how heterogeneity inside the scale of a wavelength is expressed in observables
Notes: Note: Design error – had expected upper limit around 500 not 1500 Hz